## Slide 1: Technology & living
Textile Technology
S3.2.2 Fabric Finishing

## Slide 2
  Definition Of Fabric Finishing
  In textile manufacturing, finishing refers to the processes that improve the look, performance or "hand feel" of the finished textile products or clothing.
  Textile finishing decides the ultimate appearance and aesthetic properties of textile materials.
  Additionally, it is able to change various physical and chemical properties of fabrics per consumer needs.
Photo(s) is/are owned and provided by HKDI.

## Slide 3
  Repellent finishes
  Finishes that repel water, oil, stains and dirt are very important for the various end uses of clothing, home and technical textiles.
  All of these properties can be achieved by suitably adjusting the hydrophilicity and hydrophobicity of fabircs.
  In recent years, there has been a large demand for easy-care fabric finishes by which multiple functional properties like crease recovery, water repellence and stain resistance can be achieved in a single step using minimal chemicals.
Photo(s) is/are owned and provided by HKDI.

## Slide 4
  Easy-care finishing
  Two of the main disadvantages of cellulosic materials is that they wrinkle and shrink after washing.
  A special kind of finish is necessary to over come these problems.
  The problem arises mainly due to swelling and breakage of hydrogen bonds of fibre knots during the wetting of the cellulose.
  Stabilising the cross-links between the fibres prevent wrinkling and creasing after wetting and reduce shrinkage due to laundering.
Photo(s) is/are owned and provided by HKDI.

## Slide 5
  Fire- retardant and flame-resistance finishes
  Flame-resistant and fire-retardant fabrics are essential safety tools in a variety of industrial and commercial applications.
  Fire-Retardant Fabric vs. Fire-Resistant Fabric
  Fire-retardant fabrics and fire-resistant fabrics are two different classes of material.
  Fire-retardant fabrics: They will burn, but at a much slower rate than untreated fabrics.
  Flame-resistant fabrics: are made up of synthetic fibres that resist ignition under exposure to flame or heat. Instead of burning, these fabrics will eventually begin to melt.
Photo(s) is/are owned and provided by HKDI.

## Slide 6
  Finishes for protection against microbial, insect and UV radiation
  Insect-resistant finishes are required to protect wool and other animal fibres from attacks by the moths and beetles.
  Mosquito-repellent textiles protects people from the bite of mosquitoes and thereby assure safety from the infectious diseases they spread. Permethrin is widely used against a wide range of pests including mosquitoes, lice, ticks, fleas, mites and black flies.
  The damaging effects of solar UV are also well known, and the development of effective UV-protective finishes is of great importance to human health, society and environment.
Photo(s) is/are owned and provided by HKDI.