## Slide 1: basic block OF Bodice

## Slide 2: Ladies Bodice
Photo(s) is/are provided by HKDI

## Slide 3: Basic block for ladies bodice
Bust/Chest | 87cm
Waist | 64cm
Scye Depth | 21.4cm
Nape to Waist | 40.3cm
Scye Width | 11.2cm
Half Back | 17.6cm
Back Neck Width | 7.4cm
Front Neck Point Height | 2.3cm
Front Neck Width | 6.1cm
Front Neck Depth | 7cm
Neck to Bust | 26cm

## Slide 4: From (1) to (0) = Scye Depth (21.4cm) From (2) to (0) = Nape to Waist + 0.3cm (40.6cm) From (6) to (1) = Half Bust +4.5cm (48cm) Square up and down from (6) to (7) & (I).

## Slide 5: (3) is midway (0)-(1). Square from (1)-(2)-(3) From (4)to(1) = Half Back (17.6cm) From (5) to (4) = Scye Width (11.2cm)

## Slide 6: From (8) to (0) = Back Neck Width (7.4cm) Square up 1.5cm for all sizes to (9). Draw the back neck in curve line.

## Slide 7: (10) is 4cm below line (0)-(7) for all sizes. Square out 2 cm to (11). Draw the shoulder (9)-(11).

## Slide 8: (12) is midway of (4) & (5). Square down to (13).

## Slide 9: (14)is approximately 3cm from (4). Draw the back scye (11)-(14)-(12) with a curve line.
Right angle

## Slide 10: From (15) to (5) =6cm for all size. Square up from (15) to (16). (16) above nape line (0)-(7)=Front Neck Point Height (2.3cm) From (21) to (7) =Front Neck Point Height (2.3cm) Square across from (21).

## Slide 11: (17) is 5cm below line (0)-(7). From (18) to (16) =(9) to (11) minus 0.3cm, measure from pitch (front shoulder line)

## Slide 12: Front pitch is 5cm for all size. Connect (18) to front pitch. (19) is midway between (18) and front pitch.

## Slide 13: (20) is approximately 2 cm from (5). Hollowing 1 cm at (19), Draw the front scye (18)-(20)-(12),
Right angle

## Slide 14: From (22) to (21) = Front Neck Width (6.1cm) From (23) to (21) =Front Neck Depth (7cm), connect (22)-(23). Hollowing approximately 2cm at (24) . Draw the front neck (22)-(23) in a curve line.

## Slide 15: (25) is midway between (5)-(6), square down from (25) to (B). From (26) to (22) =Neck to bust measure from (22), on to line (25)-(B).

## Slide 16: Join the front bust dart.

## Slide 17: Find the midway point of the half back line (3). (27) is 2 cm toward the scye. Square down from (27) to (A).

## Slide 18: From (28) to (9) =Approximately 6cm. From (28), make a small dart of 0.3CM. Connect the dart at (27).

## Slide 19: Mark 2.5cm at each side of (A), and draw 2 vertical lines. (C) & (D) are 0.4cm below waistline. Connect (C) & (D) to (27).

## Slide 20: Mark 2 cm each side of (13). Draw back waist (2)-(C) and (D)-(E), hollowing slightly.

## Slide 21: Mark 2.5cm at each side of (B) and draw 2 vertical lines. (G) & (H) are 1.2cm below waistline. Connect (G) & (H) to (26). Draw the side seams (E) to (12) & (F) to (12). Draw waistline (F)-(G) with a slight curve. (I) is 0.8 cm below waistline. Connect (I) & (H) with a slight curve.

## Slide 22
Finished the Ladies Bodice Tops ( front and back )

## Slide 23: Demonstration Videos
Basic block for ladies bodice - Part 1
Basic block for ladies bodice - Part 2

## Slide 24
Men’s
bodice

## Slide 25: Basic block for Men’s bodice
Chest | 100cm
Scye Depth | 24.4cm
Neck Size | 40cm
Half Back | 20cm
Natural Waist Length | 42.2cm
Shirt length | 80cm

## Slide 26
Square both ways from (0).
(0)-(5) = (1)-(4)  ½ chest plus 8cm (58cm)
(0)-(3) = Shirt Length plus 1cm.
26.9cm
80cm
1
58 cm

## Slide 27
(0)-(2)= Natural Waist Length plus 1cm (43.2cm); square across
(0)-(7)= ½ Scye Depth plus 1cm (13.2cm); square out
(0)-(8)= ½ measurement of (0)-(7) (6.6cm); square out
2

## Slide 28
(1)-(11) = half back plus 2.5cm (22.5cm); square up to (12) and (13)
5
11
2

## Slide 29
(0)-(9) = 1/5 Neck Size minus 0.5cm (7.5cm); square up
(9)-(10) = 2cm
5
9
10
11

## Slide 30
(13)-(14) = 3.5cm; square out
(14)-(15) = 1.5cm
5
14
15
11

## Slide 31
Join (10)-(15)
(0)-(10): draw in neck curve
5
11

## Slide 32
(1)-(16) = 1/3 Chest plus 1.5cm (34.8cm)
5

## Slide 33
(5)-(17) = 1/5 Neck Size minus 1cm (7cm)
(5)-(18) = 1/5 Neck Size (8cm)
5

## Slide 34
(15)-(19) = 2cm; square out
5

## Slide 35
(17)-(20) = the measurement (10)-(15) plus 0.5cm (17.8cm)
5
20

## Slide 36
(16)-(21): square up 3.5cm from (16)
5

## Slide 37
Join (20)-(21)
5

## Slide 38
(21)-(22) = 1/3 measurement of
(20)-(21)
(16)-(23) = ½ measurement of (11)-(16) minus 0.5cm (5.6cm)
Square sown to hem line
5
23
2

## Slide 39
(11): Mark a line 3cm at 45 degree
(16): Mark a line 2cmat 45 degree
5

## Slide 40
(22): Curve inwards 1.25cm
Join the armhole
5

## Slide 41
5

## Slide 42: Demonstration Video
Basic block for men’s bodice

## Slide 43
Royalty-free photo sourced from www.pexels.com
Chapter Activity
Construct basic block of the ladies or men’s bodice
Photo(s) is/are provided by HKDI