## Slide 1: Introduction to pattern drafting and sewing

## Slide 2: Introduction to pattern drafting and sewing
(1)
(3)
Source from royalty free photo from Pexels
Source from royalty free photo from Pexels
Source from royalty free photo from Pexels

## Slide 3: Safety Rules
Source from royalty free photo from Pexels

## Slide 4
Feet should be removed from the treadle / foot pedal when not machining.
Source from royalty free photo from Pexels
Treadle

## Slide 5
Source from royalty free photo from Pexels
Scissors, needle and other sharp equipment should be handled with care and placed safely on worktops and tables.
Always keep fingers away from the needle and belt while the sewing machine is running.

## Slide 6
Long hair must be tied back.
Source from royalty free photo from Pexels
Source from royalty free photo from Pexels

## Slide 7
Source from royalty free photo from Pexels
Never interfere with the motor or moving parts of the sewing machine.
Guards and other safety devices are there to protect the users and should not be removed.

## Slide 8: Tools and equipment for Making patterns

## Slide 9: Dress stand
Source from royalty free photo from Pexels

## Slide 10: Paper (marker paper and Card board paper)
Source from royalty free photo from Pexels

## Slide 11: Tape measure/ Yard stick / Grading ruler
Source from royalty free photo from Pexels

## Slide 12: Set square / Curve rulers
Source from royalty free photo from Pexels

## Slide 13: Pencil / Marking chalks / Cutting shears / Notcher
Source from royalty free photo from Pexels

## Slide 14: Tracing wheel/ Pattern weight / Work table
Source from royalty free photo from Pexels

## Slide 15: Introduction to pattern cutting techniques
(1)
(3)
Source from royalty free photo from Pexels
Source from royalty free photo from Pexels

## Slide 16: Grain Lines
Grain:
The direction of the yarn in woven fabrics. The direction affects the look feel of the fabric, and the hang and appearance of the garment.
Lengthwise grain (straight/warp ):
Yarns that are woven parallel with the selvage and twisted more tightly than the crosswise grain. Also called the straight grain.
Crosswise grain (cross/ weft):
Yarns that are woven perpendicular to the selvage.
True bias:
A diagonal line that intersects with the lengthwise and crosswise grains at a 45° angle. The bias has maximum stretch.
True bias
(45° angle)

## Slide 17: Effects of different grain line positions on clothing design:
A ) Straight grain ( warp ) is stronger and stable. The straight grain can control the shape and hang of garment.
B ) Crosswise grain (weft) is woven perpendicular to the straight grain and is less stable.
C) True bias runs at 45° to the straight grain and crosswise grain, and causes fabric to stretch when cut.
A
C
B

## Slide 18: The Effect of Pattern's Grain on Fabric
The fabric’s grain can affect the appearance, hang, and fit of the garment.
The grain line on the pattern is always placed on fabric parallel with the selvage.

## Slide 19: Seam allowance
Different areas / lines / curves add different amount of seam allowance
Curve line adds less seam allowance
Hem adds more seam allowance

## Slide 20: Seam allowance
The amount of seam allowance varies according to the following factors:
Method of manufacture
Type of fabric
Type of style of garment

## Slide 21: Notch
Indicates how different pattern pieces of a garment are matched to each other, as well as the placement of their darts, zippers, seam lines, hems and other design details.

## Slide 22: Notch
The marks are made inside the seam allowance at right angle to the seam line, and extend all the way to the pattern edge.

## Slide 23: Balance Marks
They are used to ensure accurate joining of garment parts.
For example: two balance marks located at back armhole while one balance mark along front armhole.

## Slide 24: Labelling
Pattern pieces are labelled to indicate the pattern name, centre front, centre back and the total number to be cut.

## Slide 25: Procedure for pattern construction
Stage One:
Analyse the designed style.
Draft / Trace basic blocks.
Adapt basic blocks to various garment styles.

## Slide 26: Procedure for pattern construction
Stage Two:
Add appropriate seam allowance
Position the grain line, balance marks and notches
Label each pattern:
  Name
  Centre Front (C.F.) and Centre Back (C.B.)
  Number of pieces to be cu
  Type of fabric in which the pattern piece will be cut (e.g. lining)
Cut out pattern pieces

## Slide 27: Preparation before sewing
Source from royalty free photo from Pexels

## Slide 28: Preparation before sewing
Turn the machine pulley and raise the thread take-up before threading the upper thread
Pass the needle thread in the order shown in the figure.
Pass the thread to the needle eye from left to right.
Pull out about 10cm (4 inches) of the thread from the needle eye.

## Slide 29: Operation the sewing machine
Turn off the power switch when threading the machine , replacing the bobbin or installing the needle.
Do not touch any of the moving parts or press any objects against the machine while sewing .
Switch off the power when not using the machine and when leaving the machine unattended.

## Slide 30: Demonstration Videos
1. PREPARATION BEFORE SEWING - UPPER THREADING
2. PREPARATION BEFORE SEWING - BOBBIN AND BOBBIN CASE
3. PREPARATION BEFORE SEWING - THREAD THE BOBBIN

## Slide 31: chapter activity
Can you try to thread the sewing machine and bobbin?
THREAD THE SEWING MACHINE
Source from royalty free photo from Pexels